## “KAVALIER 800”

Designed by Albert Nazarov, Maxim Kovalyov, Dmitry Dolinsky

Published in “Power & Sail Boats” magazine:

Nazarov A., Kovalyov M., Dolinsky "T800 by own hands" // "Power & Sail Boats", St.Petersburg, 2003, No.1 (188) – p.122-125. and No.2 (189) – p.122-125. (in Russian).

Main particulars

| LOA, m | 8.00 |
| --- | --- |
| LWL, m | 8.00 |
| Beam, m | 2.50 |
| Draught, m | 0.63 / 2.00 |
| Empty weight, DSPL, kg | 1200 |
| Sail Area, SA, m2: |  |
| - main | 30.0 |
| - jib | 13.5 |
| - gennaker | 38 |
| Dimensionless parameters: |  |
| L/DSPL1/3 | 7.52 |
| SA1/2/DSPL1/3 | 6.21 |
| Prismatic coefficient, CP | 0.57 |
| LCB, % | 3.5 |

GENERAL ARRANGEMENT:

1- forepeak; 2 – double berth; 3 – hanging locker; 4 - head; 5 - galley; 6 - sofa; 7 - seat; 8 – chart table; 9 - berth; 10 - locker; 11 – gas bottle locker; 12 – outboard motor compartment; 13 - table; 14 - cockpit; 15 - pillar

SAIL PLAN:

Spar: mast section - 130(80(2.5 mm, top 100(80(2.5 mm, aluminum alloy; boom - pipe 120(2 mm, aluminum alloy; bowsprit - pipe 80(2 mm, aluminum alloy; spreaders - pipe 28(3, aluminum alloy; Standing rigging: lower shrouds - cable 1(19, d=5; intermediate shrouds - cable 1(19, d=4; upper shrouds - cable 1(19, d=4; forestay - cable 1(19, d=5; afterstay - cable 1(19, d=4; runners - cable 1(19, d=4;